## Slide 1
Brain Tumor Volumetric Segmentation on MRI
Automated 3D delineation of the tumor via MRI modalities.
A fast 2D detector finds the tumor a promotable video model refines it in 3D.
BraTS 2024 adult glioma, 1,621 MRI scans.
One slice: the MRI picture · YOLO's hint · YOLO's own mask · MedSAM2's answer (green = found, red = extra)

## Slide 2
BACKGROUND
Why segment brain tumors automatically?
2
• Gliomas are the most common malignant primary brain tumors in adults.
• Doctors outline the tumor on MRI to plan surgery and radiotherapy and to track change between scans.
• Outlining by hand is slow: a scan has well over a hundred slices, each drawn separately.
• Experts don't agree perfectly with each other, so outlines vary between readers.
• Automation goal: a fast, consistent 3D outline a doctor only needs to check.
An expert outline on FLAIR (green = swelling, yellow = surgery cavity)
Key takeaway: Automatic 3D segmentation saves expert time and makes tumour measurements consistent.

## Slide 3
Radiologists' questioner
Question & response options | Answer A | Answer B
Q1 Years of experience reading brain MRI Options: In training (resident) · Less than 5 years · 5–10 years · 11–20 years · More than 20 years | In training (resident) | More than 20 years
Q2 Roughly how many brain-tumor cases do you read or contour per week? Options: Less than 1 · 1-5 · 6-15 · 16-30 · More than 30 | 1-5 | Less than 1
Q3 In your experience, how similar or different are tumor outlines drawn by different radiologists for the same case? Scale: 1 = Very similar → 5 = Very different | 3 / 5 | 5 / 5 Very different
Q4 How willing are you, in principle, to let a tool do the first outline and then correct it? Scale: 1 = Not at all willing → 5 = Very willing | 5 / 5 Very willing | 5 / 5 Very willing
3

## Slide 4
BACKGROUND · PATIENT BRATS-GLI-00046-101, SLICE 115, ZOOMED ON THE TUMOUR
Each MRI sequence shows a different part of the tumour
4
T1 (no contrast)
Rim (ET, violet) barely visible. Not used by our models.
T1C (with contrast)
Rim lights up (ET, violet); dead core dark (NETC, red).
T2
Swelling and fluid bright (SNFH, green).
FLAIR
Like T2, but brain fluid is dark: swelling stands out.
Expert labels
NETC red · SNFH green · ET violet · RC (cavity) yellow
• Target: the whole tumour (all four parts). Our models see T1C, T2 and FLAIR as one colour picture.
• Score: 3D Dice = 2 × overlap ÷ (model + expert), from 0 to 1, per patient.
Key takeaway: No single sequence shows the whole tumour, so the models look at several sequences together.
Notes: כאן רואים מטופל אחד, BraTS-GLI-00046-101, בפרוסה 115, בהגדלה על אזור הגידול. בפרוסה הזאת מופיעים כל ארבעת חלקי הגידול.
T1 (בלי חומר ניגוד): אפשר לראות את האזור הפעיל של הגידול, אבל לא בצורה ברורה.
T1C (עם חומר הניגוד גדוליניום): במקומות שבהם מחסום הדם-מוח (BBB – Blood–Brain Barrier) פגוע, כלי הדם דולפים והגדוליניום מצטבר ברקמה, ולכן היא נראית לבנה. לדוגמה, הטבעת הלבנה היא רקמת הגידול הפעיל (ET). כאן אפשר לראות גם את הליבה הנמקית (Necrotic core, NETC), החלק המת של הגידול, שנשאר כהה במרכז.
T2 ו-FLAIR: שניהם מבליטים את הבצקת והנוזלים. ב-FLAIR הנוזל הרגיל של המוח (בחדרים) נראה כהה, ולכן הבצקת בולטת יותר.
בחלק הצהוב: חלל הניתוח (Resection cavity, RC), המקום שממנו הוסר הגידול בניתוח.
אנחנו מסמנים את הגידול כולו, כלומר את כל החלקים יחד. המודלים שלנו מקבלים את T1C, T2 ו-FLAIR כתמונה צבעונית אחת.
המדד: 3D Dice, החפיפה בין המסכה של המודל לזו של המומחה בכל הנפח. 0 = אין חפיפה, 1 = מושלם.
מסר: אף רצף לבד לא מראה את כל הגידול, ולכן משלבים כמה רצפים.

## Slide 5
METHOD · PATIENT BRATS-GLI-00046-101, SLICE 115
Normalization: raw MRI values to one colour picture
5
• MRI has no fixed units: each sequence and scan has its own scale (here T1C up to 10,205, FLAIR up to 2,370).
• Per slice and per sequence, brain voxels only: the 0.5th percentile → 0, the 99.5th → 255, the rest clipped.
• T1C, T2 and FLAIR become red, green and blue: the same 8-bit picture for both models.
• YOLO scales it to 0–1 at 512 px. MedSAM2: ÷ 255, stretched to 512 × 512, then ImageNet mean/std, as SAM2 was pretrained.
Key takeaway: every slice is scaled on its own, so all scanners and sequences land on the same 0–255 range.
Notes: נרמול: איך הופכים את ערכי ה-MRI הגולמיים לתמונה אחת שהמודלים יכולים לקרוא.
ל-MRI אין יחידות קבועות. כל רצף וכל סריקה מגיעים בסקאלה משלהם: בפרוסה הזאת T1C מגיע עד 10,205, ו-FLAIR רק עד 2,370. משמאל רואים את שלושת הרצפים על אותה סקאלה, ו-T2 ו-FLAIR כמעט שחורים.
לכן כל פרוסה וכל רצף מנורמלים בנפרד, ורק על פיקסלים של המוח. האחוזון ה-0.5 הופך ל-0 והאחוזון ה-99.5 הופך ל-255, וכל מה שמעבר נחתך. בהיסטוגרמה רואים את שני הקווים עבור FLAIR: 74 ו-2,032. כך כמה פיקסלים בהירים במיוחד לא משבשים את כל התמונה.
אחר כך T1C, T2 ו-FLAIR הופכים לאדום, ירוק וכחול, ונוצרת תמונה צבעונית אחת של 8 ביט, אותה תמונה לשני המודלים.
YOLO מכווץ אותה לטווח 0 עד 1 בגודל 512. MedSAM2 מחלק ב-255, מותח לגודל 512 על 512, ומנרמל לפי הממוצע וסטיית התקן של ImageNet, כמו ש-SAM2 אומן במקור.
הערה כנה: הנרמול הוא לכל פרוסה בנפרד, כך שהבהירות יחסית לפרוסה עצמה. נרמול לכל הנפח היה עקבי יותר בין פרוסות, וזה לא נבדק.
מסר: כל פרוסה מנורמלת לעצמה, כך שכל הסורקים והרצפים מגיעים לאותו טווח 0 עד 255 לפני שהמודלים רואים אותם.

## Slide 6
YOLO11-seg: one slice in, shapes out
6
Input: one slice as a colour picture (red = T1C, green = T2, blue = FLAIR), 512 × 512
YOLO11-seg
medium model 2D, slice by slice
Output: for every shape a box, a confidence (0–1) and a mask
• Sees one 2D slice at a time, with no memory of the slices around it.
• Finds each tumor shape and gives it a confidence from 0 to 1.
• We keep every shape at 0.05 or more, on this slice: 0.75 and 0.35.
• Fine-tuned from a model pretrained on everyday photos (yolo11m-seg).
Key takeaway: YOLO turns each slice into shapes with confidences, fast, but blind to the slices around it.
Slice by slice on two test patients: BraTS-GLI-02621-100 (left) and BraTS-GLI-02285-102 (right)

## Slide 7
MedSAM2: three inputs, one corrected mask
7
1. The picture
the same colour slice
2. YOLO's hint
how sure YOLO is, per pixel
3. Memory
start slice + the last 6 slices
MedSAM2
SAM2 trained on medical scans
Output: the corrected mask
0.882
Dice on this slice (YOLO alone 0.852)
• Goes up, then down from the start slice; each answer joins the memory.
• 39 M weights: image encoder 70%, memory 19%, mask decoder 11%.
Key takeaway: MedSAM2 combines the picture, YOLO's hint and its memory into a corrected mask per slice.

## Slide 8
DATA
Data: 1,621 scans from 731 people, split by person
8
• Five pools: YOLO train 471 · YOLO val 81 · MedSAM2 train 500 · MedSAM2 val 245 · test 324 scans.
• No person is in both a YOLO pool and a MedSAM2 pool, so MedSAM2 trains on hints YOLO made for people it never saw, like real use.
• Pool sizes set by learning curves: MedSAM2 barely improved past 500 patients (250 → 500 → 721: 0.884 → 0.886 → 0.886), while YOLO still gained from more data.
• Caveat: test shares some people (other scans) with training pools, from the original split; kept so all test scores stay comparable.
Key takeaway: Keeping the two models' people apart makes MedSAM2's training hints realistic.

## Slide 9
METHOD · PATIENT BRATS-GLI-00046-101, SLICE 120
YOLO's hint vs YOLO's own mask
9
1 · YOLO hint
7 shapes: 0.90 is kept by both; 0.06–0.23 only in the hint
2 · YOLO's own mask
blue = mask, green line = expert
3 · Only in the hint
orange: weak shapes + the faint edge of the strong one
YOLO hint · shapes ≥ 0.05
• A probability per pixel, 0 to 1: how sure YOLO is that the pixel is tumour.
• Gives MedSAM2 more information, including YOLO's weaker guesses.
YOLO's own mask · shapes ≥ 0.25
• A yes/no answer per pixel: tumour when its probability is above 0.5.
• YOLO's final answer, used only to compare against MedSAM2.
• On this slice: hint 3,800 px · own mask 2,638 px · expert 2,570 px.
• Of the 1,162 pixels only in the hint, just 99 are real tumour: MedSAM2 has to learn which extra guesses to trust.
Key takeaway: The hint carries everything YOLO suspects; the own mask is only YOLO's confident final answer.

## Slide 10
METHOD · PATIENT BRATS-GLI-00046-101, SLICE 115
The hint, step by step
10
A · Store: YOLO's probability per pixel (0–1) is saved as 0–255.
B · Logit: ln(p / (1 − p)) gives −5.5 … +5.5, where 0 = 50%.
C · × 8: now about −44 … +44.
D · 'Nothing here' = −20: every slice with no YOLO shape (68 of 137 here) and everything outside the head.
Inside the head = any of T1C, T2, FLAIR is not 0.
All 150,618 non-zero pixels YOLO gave this patient (all slices): mostly 'sure' or 'barely'
p | 0.00 | 0.05 | 0.25 | 0.50 | 0.75 | 0.95 | 0.99 | 1.00
Stored | 0 | 13 | 64 | 128 | 191 | 242 | 252 | 255
Logit | −5.54 | −2.92 | −1.09 | 0 | +1.09 | +2.92 | +4.43 | +5.54
Logit × 8 | −44 | −23 | −9 | 0 | +9 | +23 | +35 | +44
Key takeaway: The hint = YOLO's confidence per pixel on MedSAM2's scale, plus a firm 'no' where YOLO saw nothing.

## Slide 11
METHOD · HINT STYLES · TEST, 324 PATIENTS, 38 M BLOB PIXELS
Two hint styles: 'max' vs 'max_weighted'
11
Patient BraTS-GLI-00046-101, slice 120: 7 YOLO shapes, confidence 0.06–0.90
• max (all our runs): YOLO's probability per pixel; the shape's confidence is ignored.
• max_weighted: probability × the shape's confidence, then the same logit × 8.
Spread of every hint value on a YOLO shape
Share of a shape saying 'tumour', by its confidence
Key takeaway: max_weighted silences every shape under 0.5 confidence and caps the rest near +24.
Notes: השוואה בין שתי דרכים להעביר את הרמז של YOLO ל-MedSAM2. כאן רק הקלט, לא מה ש-MedSAM2 עושה איתו.
max, מה שהשתמשנו בו בכל הריצות: לכל פיקסל ההסתברות של YOLO, והביטחון של הצורה לא נכנס.
max_weighted: ההסתברות כפול הביטחון של הצורה, ואז אותו לוגיט כפול 8.
בגרף העליון: ב-max כמעט חצי מהפיקסלים מקבלים את הערך המקסימלי, 44+. ב-max_weighted אין אף פיקסל מעל בערך 24+, כי הביטחון הכי גבוה הוא בערך 0.9.
בגרף התחתון: כל צורה עם ביטחון מתחת ל-0.5 הופכת ב-max_weighted ל'לא גידול' לגמרי, כי הסתברות כפול ביטחון לא יכולה לעבור 0.5. ב-max אותן צורות עדיין אומרות 'גידול' ב-40% עד 63% מהפיקסלים.
שימו לב: 77% מפיקסלי הצורות הם בצורות עם ביטחון מעל 0.75, אז רוב הרמז כמעט לא משתנה, חוץ מהעוצמה.

## Slide 12
METHOD · TEST PATIENT BRATS-GLI-00008-101, SLICE 78
The mirror check
12
Normal patient
Mirrored
MedSAM2
both copies in one batch
• Same batch: the normal and the left ↔ right mirrored patient go through both MedSAM2 passes together.
• Flip back: the mirrored answer is flipped left ↔ right so it lines up with the normal one.
• Average per pixel: the two scores are averaged, then the 50% cut-off makes the final mask.
Normal answer
Mirror, flipped back
Where they disagree
Averaged result
3D Dice, this patient
normal 0.8457 · mirrored 0.8554 · averaged 0.8524
The two answers differ on only 1,312 voxels, all at the tumor edge (yellow).
Result colours: green = found · yellow = missed · red = drawn, not tumour

## Slide 13
METHOD · TRAINING
MedSAM2 fine-tuning: which parts we train
13
MedSAM2’s architecture
• Image encoder: the biggest part (27 M of 39 M weights). SAM2 trained it on millions of images and MedSAM2 tuned it on medical scans, its features are already good and our data is small.
• Prompt encoder: has never seen a soft YOLO hint.
• Mask decoder: must learn to trust the hint where it's right and override it where it's wrong.
• Memory: must learn to carry the tumour from slice to slice.
Part | Job | Weights | % | Rate
Image encoder | Looks at the slice picture | 27.2 M | 69.9% | 1e-6 *
Memory attention | Mixes in memory of earlier slices | 5.9 M | 15.2% | 1e-5
Mask decoder | Draws the final mask | 4.2 M | 10.8% | 1e-4
Memory encoder | Stores each finished slice | 1.4 M | 3.6% | 1e-5
Prompt encoder | Reads YOLO's hint | 6,220 | 0.02% | 1e-4
Small extras | Bookkeeping | 18,993 | 0.05% | frozen
Total |  | 39.0 M | 100% | 
What trains | Size | Val | Test | Gain | Better/worse | Time
decoder + prompt | 4.4 M | 0.8910 | 0.8970 | +0.0141 | 172 / 17 | 2 h 24
+ memory | 11.7 M | 0.8918 | 0.8981 | +0.0152 | 198 / 19 | 2 h 27
all (+ image encoder) | 38.9 M | 0.8917 | 0.8997 | +0.0168 | 206 / 14 | 8 h 29
+ memory, −20 (final) | 11.7 M | 0.8928 | 0.8988 | +0.0159 | 200 / 17 | 3 h 01
• * the image encoder trains only in 'all'. Gain = test Dice over the YOLO hint (0.8828).
• Final run (bold): best on val (0.8928). Settings were chosen on val, never on test: 'all' scores higher on test but tied on val and took 3.5× longer.

## Slide 14
RESULTS
Results: MedSAM2 beats YOLO's best on test
14
• 0.8988 vs 0.8834 mean 3D Dice on the same 324 test patients.
• 185 patients better, 18 worse (by more than 0.01), the rest about the same.
• Found 96.9% of tumor slices and kept 96.4% of empty slices empty.
• Settings were picked on val, test was scored once.
Key takeaway: Adding MedSAM2 gives a consistent, statistically clear gain over the best YOLO.

## Slide 15
RESULTS
Where it works, and where it struggles
15
Mean MedSAM2 3D Dice by side (rows) and tumour size (columns), test
• Size matters, side doesn't: about 0.67–0.73 for tumors under 10 mL vs about 0.93 for 100 mL and up, left ≈ right.
• The biggest gains over YOLO are on small tumors.
• Slice by slice (bottom): MedSAM2 follows the tumor through memory and rejects YOLO's isolated false alarms.
Key takeaway: Tiny tumors remain the weak spot, and they are where MedSAM2 helps most.
Where the tumour centres are, seen from above
Right side
Both sides
Left side

## Slide 16
EXPERIMENTS · WHAT-IF TEST (VAL, 245 PATIENTS)
What if the start slice were perfect?
16
The test: same trained MedSAM2, no retraining. Start slice gets the expert mask; all other slices keep YOLO's hint.
How it runs
YOLO
YOLO
YOLO
YOLO
Expert
YOLO
YOLO
YOLO
YOLO
◀ memory carries it up
and down ▶
Start slice: the expert mask (fully sure)
All other slices: YOLO's hint, as usual
A what-if only: the expert mask is never available when predicting.
+0.0047
val 3D Dice 0.8928 → 0.8975
173 / 1
patients better / worse
Gain over today's pipeline (val)
Best confidence idea (blob → 'don't know')
+0.0012
Expert mask on the start slice
+0.0047
Key takeaway: one correct slice, carried by memory, adds +0.005 Dice: 4× the best confidence idea.
Notes: ניסוי "מה אם": מה קורה אם פרוסת ההתחלה מושלמת?
לקחנו את אותו MedSAM2 מאומן, בלי אימון מחדש, ושינינו דבר אחד בלבד: בפרוסת ההתחלה, שממנה המודל מתחיל לעקוב למעלה ולמטה, נתנו לו את סימון המומחה במקום הרמז של YOLO. כל שאר הפרוסות קיבלו את הרמז של YOLO כרגיל.
על 245 מטופלי הוולידציה ה-3D Dice עלה מ-0.8928 ל-0.8975, כלומר 0.0047+. 173 מטופלים השתפרו ורק אחד הורע.
זה פי 4 מהרעיון הטוב ביותר שבדקנו לשימוש בביטחון של YOLO. חלק מהשיפור הוא הפרוסה עצמה, והשאר הוא הזיכרון שמעביר את ההתחלה הנכונה לפרוסות השכנות.
חשוב: זה ניסוי בלבד. בזמן חיזוי אמיתי אין לנו את סימון המומחה. המסר הוא שהתחלה טובה שווה הרבה.

## Slide 17
RESULTS · TEST, 324 PATIENTS
Separate tumour pieces: MedSAM2 needs YOLO to see them
17
35 of 324 patients (11%) have tumour pieces that share no slice. The start slice is in the largest piece in 33 of them.
What MedSAM2 faces
start
largest piece
empty slices
other piece
• Memory passes the tumour from slice to slice.
• Across empty slices there is nothing to pass on, so the next piece must come from YOLO's hint.
Did MedSAM2 find the piece?
Largest piece
35 / 35
Other piece, YOLO hinted it
7 / 9
Other piece, YOLO missed it
0 / 7
Other pieces of 100+ voxels only; 26 specks under 100 voxels left out.
Lost 2 that YOLO found well (707 and 277 voxels).
Key takeaway: MedSAM2 finds a separate piece only when YOLO hints it; memory can't jump across empty slices.
Notes: בדקנו מה קורה כשלגידול יש כמה חלקים נפרדים, כלומר חלקים שאין ביניהם אף פרוסה משותפת.
זה קורה ב-35 מתוך 324 מטופלי המבחן, 11%. ברוב המקרים פרוסת ההתחלה נמצאת בחלק הגדול.
את החלק הגדול MedSAM2 מוצא תמיד, 35 מתוך 35.
בחלקים האחרים, בגודל 100 ווקסלים ומעלה: כש-YOLO נתן רמז על החלק, MedSAM2 מצא 7 מתוך 9. כש-YOLO פספס את החלק, MedSAM2 פספס את כל השבעה.
הסיבה: הזיכרון מעביר את הגידול מפרוסה לפרוסה, אבל בפרוסות הריקות שבין החלקים אין מה להעביר, ולכן החלק הבא חייב להגיע מהרמז של YOLO.
בשני מקרים MedSAM2 איבד חלק ש-YOLO מצא היטב; את הסיבה עוד לא בדקנו.

## Slide 18
EXPERIMENTS · TEST, 324 PATIENTS
Should the surgery cavity count as tumour?
18
Our target counts the resection cavity (RC) as tumour: 17% of all tumour voxels; 270 of 324 test patients have one.
What counts as tumour
Today
NETC
SNFH
ET
RC
Proposed
NETC
SNFH
ET
0 · bg
Dead core · Swelling · Enhancing · Cavity
• The cavity is the hole left by surgery, not tumour.
• BraTS 2024: whole tumour = NETC + SNFH + ET.
• Fix: RC → background (0), retrain both models.
MedSAM2 3D Dice if RC → background
Today (cavity counted)
0.899
Same model, no retraining
0.773
Best case: cavity skipped perfectly
0.870
Realistic after retraining (estimate)
≈ 0.85–0.86
Bars start at 0.70. YOLO drops alike (0.883 → 0.853): MedSAM2's lead holds.
Key takeaway: without the cavity the task is honest but harder: ~3 Dice points lower, not a worse model.
Notes: בשקף הזה אנחנו שואלים: האם חלל הניתוח צריך להיחשב כגידול?
היום המטרה שלנו היא כל תווית שאינה אפס, כולל תווית 4 – חלל הניתוח (RC). זה 17% מכל וקסלי הגידול, ו-270 מתוך 324 מטופלי הטסט הם אחרי ניתוח.
החלל הוא החור שנשאר אחרי הוצאת הגידול – נוזל או דם – ולא גידול. גם בהגדרה של BraTS 2024, 'הגידול השלם' הוא NETC + SNFH + ET, והחלל נמדד בנפרד. לכן ההצעה: להפוך את החלל לרקע (0) ולאמן מחדש.
מה יקרה ל-Dice? מדדנו על 324 מטופלי הטסט: היום 0.899. אותו מודל בלי אימון מחדש – 0.773, כי הוא עדיין מסמן את החלל. גם אם המודל ידלג על החלל בצורה מושלמת – 0.870. החלל גדול וקל (המודל מוצא 91% ממנו), ומה שנשאר הוא טבעת דקה של בצקת סביבו, שקשה לסמן. אחרי אימון מחדש אנחנו מעריכים 0.85–0.86.
YOLO יורד באותה מידה, כך שהיתרון של MedSAM2 (כ-1.7 נקודות) נשמר.
המסר: הורדת החלל הופכת את המשימה לכנה יותר וקשה יותר – הציון יורד כי המטרה קשה יותר, לא כי המודל גרוע יותר.

## Slide 19
NEXT STEPS
Future work
19
Sharper edges
• Average several trained MedSAM2 runs (an ensemble), with no new training.
• Edge-focused training loss.
• Finer output: scans are 182 × 218, the model works at 512 × 512.
Hints & small tumours
• Replace YOLO with a 3D nnU‑Net as the hint maker: the final score follows the hint quality.
• Weigh hint pixels by shape confidence ('max_weighted').
• Give YOLO 3D context (neighbouring slices).
• Train more on tumours under 10 mL.
Beyond this project
• Predict the tumour parts (ET, NETC, SNFH), not only the whole tumour.
• Test on other hospitals' scans.
• Remove the test/train people overlap; measure speed.
Key takeaway: Next gains come from sharper edges and small tumours, then proving it on outside data.

## Slide 20
NEXT STEPS
Future work: fewer missed and false slices
20
Fewer false slices
• Smooth YOLO across neighbouring slices, so a one-slice false alarm fades before it becomes a hint.
• Let MedSAM2's 'tumour here?' score wipe empty slices (the switch is in the code, not yet tested).
Hints & small tumours
• Multiply each pixel of the hint by its shape’s confidence, so a 0.06 shape becomes faint instead of as loud as a 0.90 one.
• Train more on tumours under 10 mL.
Much more data
• Train on much more data sets: other BraTS collections and other hospitals' scans.
• YOLO still improved with more data; MedSAM2 had levelled off.
Key takeaway: cleaner hints, more small tumours and much more data should cut missed and false slices.
The problem (test): 672 of 21,910 tumour slices missed (3.1%) · 815 of 22,663 empty slices drawn on (3.6%).
Notes: עבודה עתידית, חלק שני: פחות פרוסות שפוספסו ופחות פרוסות שגויות.
הבעיה, על קבוצת המבחן: MedSAM2 פספס 672 מתוך 21,910 פרוסות עם גידול, כ-3%, וסימן גידול ב-815 מתוך 22,663 פרוסות ריקות, כ-3.6%.
פחות פרוסות שגויות: להחליק את הפלט של YOLO בין פרוסות שכנות, כך שהתראת שווא שמופיעה בפרוסה אחת בלבד תיחלש לפני שהיא הופכת לרמז. ובנוסף, לתת לציון 'יש כאן גידול?' של MedSAM2 למחוק פרוסות ריקות. המתג כבר קיים בקוד, אבל עוד לא נבדק.
רמזים טובים יותר וגידולים קטנים: להכפיל כל פיקסל ברמז בביטחון של הצורה שלו, כך שצורה עם ביטחון 0.06 תהיה חלשה ולא חזקה כמו צורה עם 0.90. ולאמן יותר על גידולים קטנים מ-10 מ"ל, שם התוצאות הכי חלשות.
הרבה יותר נתונים: לאמן על מאגרים נוספים, אוספים אחרים של BraTS וסריקות מבתי חולים אחרים. YOLO עוד השתפר כשהוספנו נתונים, בעוד ש-MedSAM2 כבר התייצב.
מסר: הצעד הבא הוא לצמצם את הפרוסות שפוספסו ואת הפרוסות השגויות, עם רמזים נקיים יותר, יותר גידולים קטנים והרבה יותר נתונים.

## Slide 21
BRAIN TUMOUR SEGMENTATION · YOLO + MEDSAM2
Thank you
Questions?